## Slide 1
Enhancing Underdrawing Visualization using Adaptive and Localized Image Analysis of Reflectance Hyperspectral Imaging Data from a 15th Century Painting
Wallace Peaslee1,2, Marta Melchiorre Di Crescenzo3, Nathan Daly3, Ingrid Daubechies1,4, Shira Faigenbaum-Golovin1, Catherine Higgit3, Barak Sober5
1. Department of Mathematics, Duke University, US. 2. Department of Computer Science, Duke University, US. 3. The Scientific Department, National Gallery, London, UK. 4. Department of Electrical and Computer Engineering, Duke University, US. 5. Department of Statistics and Data Science, The Hebrew University of Jerusalem
GitHub Repository
1
2
3
4
5
6

## Slide 2: Click Here For Instructions
Click a portion of the poster to learn more relevant information.
Clicking will bring you to a few slides.
Once you have completed the small set of slides, you will return to the main poster automatically
Please have the presentation in “Presenter mode” for this poster to function properly.

## Slide 3: The Adoration of the Kings
The Adoration of the Kings is a tempura on wood painting completed by Sandro Botticelli and Filippino Lippi around 1472.
We use details of this work as a case study for methods to enhance visualization concealed underdrawings.
Return to poster
More details

## Slide 4: The Adoration of the Kings
The Adoration of the Kings is a tempura on wood painting completed by Sandro Botticelli and Filippino Lippi around 1472.
We use details of this work as a case study for methods to enhance visualization of concealed underdrawings.
Return to poster
More details

## Slide 5: The Adoration of the Kings
Sandro Botticelli (about 1445 – 1510) and the young Filippino Lippi (about 1457 – 1504) collaborated on this work. The crowd on the left is characteristic of Boticelli’s work, while the figures in the central foreground are most likely done by Filippino.
The painting may have been made as part of a piece of furniture and reflects the popularity of the Adoration of the Kings in Florence.
Any other details I should highlight/include?
The Adoration of the Kings

## Slide 6: Concealed Underdrawings Problem

## Slide 7: Concealed Underdrawings Problem
Reflectance imaging spectroscopy, around 2000nm.
We use reflectance hyperspectral imaging data to provide visualizations of concealed underdrawings.
  Shortwave infrared wavelengths (SWIR).
Challenges:
  High dimensionality of hyperspectral data.
  Spatial heterogeneity of paintings.
Return to poster
More details

## Slide 8: Concealed Underdrawings Problem
Different parts of the underdrawing may be more or less legible in certain wavelength ranges.
Reflectance imaging spectroscopy, around 2000nm.
Reflectance imaging spectroscopy, around 1870nm.

## Slide 9
The SWIR reflectance hyperspectral imaging data includes over 500 bands between 1000 nm and 25000 nm.
Preprocessing step: remove rows of noise with extreme values.
  A few bands from the dataset include rows of pixels with extreme values.
  The rows are automatically detected (via a threshold when compared to the same row of nearby bands in the hyperspectral cube).
  The rows of extreme values replaced with a linear interpolation of the same rows from adjacent bands in the hyperspectral cube.
Concealed Underdrawings Problem

## Slide 10
Localizing PCA

## Slide 11
Principal Component Analysis (PCA) is a global dimension-reduction method that can be beneficial for underdrawing enhancement.
The hyperspectral cube is projected onto the first Principal Components (PCs) below.
Localizing PCA
1
2
3

## Slide 12
We can spatially localize PCA, taking into account the heterogeneity of the painting and utilizing spatial information.
Localizing PCA
Global PCA result.
The hyperspectral cube is projected onto the first principal component.
Local PCA result.
Each pixel of the hyperspectral cube is projected onto its first local principal component (which is computed using pixels within a 100-pixel radius).

## Slide 13
Localizing PCA
Weighted pixels
To compute the local PCA, we use a pixel-by-pixel (or window-by-window) approach.
For each pixel, we spatially weight the hyperspectral cube by distance to that pixel and run PCA on that weighted neighborhood.

## Slide 14
Local PCA is motivated by spatial heterogeneity in paintings, especially arising from differences in overlying pigments.
Moreover, local PCA aims to automatically include the best underdrawing visualization in a single image and provide consistency across regions of a painting.
We see that using local spatial information can be beneficial for the PCA method, increasing underdrawing line legibility under paint passages containing pigments with different compositions.
Localizing PCA

## Slide 15
MNF and Local MNF
Maximum Noise Fraction

## Slide 16
The Maximum Noise Fraction (MNF), like PCA, is a global dimension-reduction method that we can use for underdrawings visualization.
The reflectance hyperspectral cube is projected onto the first MNF components below.
1
2
3
MNF and Local MNF

## Slide 17
MNF and Local MNF
The MNF transform aims to maximize the signal-to-noise ratio of projections (rather than variance as in PCA).
Often underdrawings are clearest in later projections onto later MNF components.
On the right is the projection onto the fourth MNF component.

## Slide 18
We can localize MNF like we localize PCA. However, for local MNF to be effective, we need to estimate noise statistics globally or with a larger neighborhood than the (weighted) pixels we consider for computing MNF components.
Global and Local MNF
Weighted pixels
Pixels used for computing local MNF noise statistics
Local MNF Result here
A local MNF result.

## Slide 19
Results
2. PCA
1. MNF

## Slide 20
Results
Global PCA
Global MNF
Local PCA
Will add Local MNF
Or otherwise
Include other results
To complete this.

## Slide 21
Perhaps a second slide of results/from another (bigger or more challenging) patch. Will add these once completed. (I could also add methods on a subset of the best bands, rather than all bands from 1000nm-25000nm.)
Maybe quantitative measurements with potential contrast would be useful? Or maybe they would be confusing?
Results

## Slide 22
We find that using local spatial information can be beneficial for the PCA method, increasing underdrawing line legibility under paint passages containing pigments with different compositions.
Local methods can provide improved consistency, especially across larger segments, as the local methods are insensitive to patch selection.
Results
Local PCA

## Slide 23
Other Methods
Potential Contrast
Spectral Derivative
Greyscale Remapping

## Slide 24
Potential contrast provides a way to quantify
Applications
  Find best bands or regions of a hyperspectral cube (next slide).
  Perform PCA or other methods on only the best bands or best regions.
  Quantify the quality of MNF or PCA projections or other results.
Potential Contrast
Sampled Underdrawings
Sampled Background
Return to poster
More details

## Slide 25
Play the video to see each band of the hyperspectral cube and the corresponding Potential Contrast value.
Notes: Botticelli and Lippi,
Adoration of the Kings
, about 1470
(NG592 for reference)

## Slide 26
I might also add spectral derivative results.
  Underdrawings stay more constant across hyperspectral bands (variance is lower), so they appear in the derivative.
  Cracks are less visible.
  Can help distinguish underdrawings from other, possibly confusing, details.
Spectral Derivative

## Slide 27
We can also remap greyscale values to improve result clarity.
Global PCA
Global PCA with greyscale remapping
Greyscale Remapping

## Slide 28
Here’s a place to put additional references or acknowledgements
References & Acknowledgements

## Slide 29
Here’s a place to put additional references or acknowledgements